## Slide 1: PERALATAN PENGUKURAN
5. Anemometer
Alat ini digunakan untuk mengukur kecepatan angin. Berbagai macam anemometer yaitu :
a. Thermo anemometer
These instruments measure the air velocity through the cooling power of the moving air. They are very use full for evaluation of heat stress because they also measure non directional, turbulent air movement which is important for heat transfer.

## Slide 2: PERALATAN PENGUKURAN
b. Anemotherm air meter (heated wire anemometer)
The instrument is self contained since the power is supplied by batteries. It’s very sensitive instruments, give fast response and can be used both for low & high air velocity as well as for temperature & static pressure measurements.
c. Alnor Thermoanemometer
This instrument measures air motion by the rate of cooling of a heated thermocouple at the tip of the probe. One thermojunction is heated by a constant current supplied to a heater wire, the other junction is located in the air stream. The air speed governs the rate of heat removal from the heated thermocouple

## Slide 3: PERALATAN PENGUKURAN
d. Rotating Vane Anemometer
Alat ini digunakan sebagai pengukur kecepatan angin yang akurat, dapat digunakan menentukan air flow melalui large supply & exhaust opening. Alat ini terdiri dari sebuah baling-baling yang dihubungkan dengan recording dials melalui roda gigi, berukuran 3,4 dan 6 inci. Pembacaan dilakukan setelah 1 menit paparan. Kecep. Angin yang dapat diukur 200 – 3000 fpm.
Kelemahan :
- tidak dapat digunakan untuk mengukur kecep. angin dalam duct.
- bukan direct reading instrument, memerlukan pencacatan waktu.
- mudah pecah, tidak boleh digunakan di tempat berdebu / bahan korosif

## Slide 4
MODEL ALAT HEAT STRESS MONITOR DIGITAL

## Slide 5: MODEL ALAT PENGUKUR MANUAL HEAT STRESS